## Slide 1: Smart Street Light System

## Slide 2: Components
Arduino UNO model …
IR for vehicle (and crowd) detection - 2
LDR for light sensing purposes - 2
LEDs – 3
Wires (males and females)
Board
Notes: Hwa 27na hn5ly el leds wra b3d tare2 wa7ed wla fel na7eten 3lshan hifr2 fe 3dd el components

## Slide 3: Implementation of Crowd detection
We can count the number of cars and using
  image processing/OpenCV techniques but it needs Raspberry pi [and analyse the density of traffic]
  IR sensor (it detects a change) (better active IR to be used or to use PIR and if it is more crowded the energy level sent will be more )
  Ultrasonic (like IR but give the distance)
  DSP with pyroelectric sensor
  Radar sensors
Notes: I would suggest you to use IR sensors on all the 4 roads of a traffic signal to detect how long the traffic congestion is. On all the roads use IR sensors after every 2-3 meters (or after every 5 cm for the demo). Now these sensors will tell you how long the traffic congestion is on any given side of the signal. You will get similar data from all the sides then using these values decide which side is more congested so you can write a logic to open the signal for that side.

## Slide 4: Elder Proposed Systems
use IR sensors to measure the traffic density. We have to arrange one IR sensor for each road; these sensors always sense the traffic on that particular road. All these sensors are interfaced to the microcontroller. Based on these sensors, controller detects the traffic and controls the traffic system.
The operating voltage of this IR transmitter & receiver is 2 to 3v. These IR (infra red) rays are invisible to the human eye. But we can view these IR rays through camera.
Limitations of this Circuit:
IR sensors sometimes may absorb normal light also. As a result, traffic system works in improper way.
IR sensors work only for fewer distances.
We have to arrange IR sensors in accurate manner otherwise they may not detect the traffic density.
Notes: Circuit Components:
ATmega8 controller
PCB board
IR sensors -4
LED’s-12(4-red,4-green,4-yellow)
12v Battery or adaptor
Serial cable
Connecting wires

## Slide 5: Elder Proposed Systems (cont’d)
the use of ultrasonic sensor for traffic flow has also been proposed. However, its challenges are the horizontal mount of sensors which makes them susceptible to interference by non-vehicular moving objects, number of sensors used for implementation, and energy consumption of modules due to system design.

## Slide 6: light sensors
The most common light sensor type used in a light sensor circuit are photoresistors, also known as Light-Dependent Resistors (LDR). Photoresistors detect whether a light is on or off and compare the relative light levels throughout the day.
Photodiodes
Notes: Light Sensor v1.2! Alongside its low price tag of $3.20 comes a highly sensitive and reliable photodiode for your light-sensing needs!
Dual OpAmp chip LM358 on board
Analog module
Onboard Grove port for easy interfacing
Convertable electrical signal output
  Depends on the ADC on your controller board, E.g. it can output 0-255 for an 8-bit ADC)
Small form factor
Recognize wider spectrum

## Slide 7
https://uge-one.com/light-sensor-module-with-ldr-and-op-amp-amplifier-3pin-digital-output-optical-sensitive-resistance-module.html?gclid=CjwKCAiAl9efBhAkEiwA4Torir2cVTV8eItAHHQKo85ZBTfPeInWfi_bcGG4PdHOgIn_7S0umLtG6RoCCuAQAvD_BwE