## Slide 2: Photocell LDR
Its default value is zero (no object obstacles) (there is light)
It outputs digital 1 when there is an obstacle to the light source
There is a potentiometer, to control the range of the sensor
Notes: https://www.electroduino.com/ldr-sensor-module-with-arduino-ldr-sensor-arduino-code/
https://www.instructables.com/LDR-Sensor-Module-Users-Manual-V10/
LDR Summary Response time of 2 – 50 ms. (Much slower than photo-transistors.) They have a “light history”. Characteristics change a little as they acclimatise after long periods in darkness.

## Slide 3
You can use the millis() function of Arduino to measure the time. This function returns the number of milliseconds passed since your board started running the current program. Therefore, to calculate the time taken by an operation, you can call millis() before and after your operation, and take the difference of the two values.
Notes: https://www.circuitbasics.com/pairing-a-light-dependent-resistor-ldr-with-an-arduino-uno/